## Slide 1
Swift Act Internship Project
Project Name : Electric Water Heater
Name : Mohamed Ahmed Awwad

## Slide 2
Hardware Configuration | 
Microcontroller | PIC16F877A
Simulation Tool | PICSimLabv0.8 PICGenios
Crystal Frequency | 8 MHz
Compiler | XC8
Hardware Mapping | 
ON/OFF Button | PORTB - PIN1
Up Button | PORTB - PIN2
Down Button | PORTB - PIN0
Heater Led | PORTB - PIN7
Hardware

## Slide 3: Kit Snapshot
Up Button
ON/OFF Button
Down Button
Heater LED
Heater
Cooler
Current Water
Temperature
7-Segment
Display
External
EEPROM

## Slide 4
a
fElectric Water Heater
I2C
DIO
ADC
Timer
Scheduler
Cooler
External EEPROM
Button
LED
Heater
Temp Sensor
Application
Service Layer
HAL
MCAL
SSD
Static Design

## Slide 5: Static Architecture
ON/OFF Button
UP Button
Down Button
Temperature Sensor
Button
Scheduler
Temperature
SSD
Heater
Cooler
External
EEPROM
SSD Display
Heater Element
Cooler Element
Heater Element
LED
Scheduling
Button States
Temperature Control
Temperature Display
EEPROM
R/W
Electric Water Heater
Button States

## Slide 6
  Scheduler
    SCH_Init_T1
    SCH_Update
    SCH_Add_Task
    SCH_Dispatch_Tasks
    SCH_Start
    SCH_Sleep
    SSD
      SSD_Init
      SSD_Update
      SSD_Display_Current_Temp
      SSD_Flash
      SSD_Display_Set_Point_Temp
      SSD_Display_OFF
    Button
      Button_Init
      Button_Update
    Heater
      Heater_Init
      Heater_Update
    LED
      LED_Init
      LED_Toggle
    Cooler
      Cooler_Init
      Cooler_Update
    External_EEPROM
      EPPROM_Init
      EEPROM_Read
      EEPROM_Write
Detailed Design

## Slide 7
Normal
Mode
System
OFF
Setting
Mode
ON/OFF Button is pressed and released / System ON
Up or Down Button is pressed
ON/OFF Button is pressed and released / System OFF
ON/OFF Button is pressed and released / System OFF
After 5 sec with press any button
System State Machine

## Slide 8
SSD Display Set point
Temp
SSD
Display
Current
Temp
SSD Flash
Set point
Temp
Up or Down Button is pressed
Up or Down Button is pressed
After 5 sec with press any button
+ current water Temp at set point Temp interval
After 5 sec without press any button
+ current water Temp out of set point Temp interval
Current water Temp
at set point Temp interval
Display State Machine

## Slide 9
ON
ON
Wait
OFF
OFF
Wait
ON/OFF Button is pressed / System OFF
ON/OFF Button is Released / System ON
ON/OFF Button is pressed / System OFF
ON/OFF Button is Released / System OFF
On/Off Button State Machine

## Slide 10
OFF
Wait
Set Point Temp
-5
Set Point
Temp
Set Point Temp
+5
(Current Water Temp < Set Point Temp ) and flag=1
/ (Heater & LED) ON (Cooler ) OFF
(Current Water Temp < Set Point Temp +5) and flag=1
/ (Heater & LED) ON (Cooler) OFF
(Current Water Temp < Set Point Temp+5 ) and flag=0
/ (Heater & LED) OFF (Cooler ) ON
(Current Water Temp < Set Point Temp ) and flag=0
/ (Heater & LED) OFF (Cooler ) ON
Temperature State Machine

## Slide 11
TASK | Actions | BCET(ms) | WCET(ms) | Period of Action(ms) | Period of Task(ms)
SSD_Update | Update SSD Display | ~0 | ~0 | 10 | 10
Temp_Get | Update Temperature sample | ~0 | ~0 | 100 | 100
Button_Update | Update System State Update SSD State | ~0 | ~0 | 150 | 150
Temp_Update | Update LED , Cooler , Heater State Update EEPROM | ~0 | ~0 | 1000 | 1000
Tick(ms) |  |  |  |  | 10
Major Cycle (ms) |  |  |  |  | 1000
Time Analysis

## Slide 12
Time
(Tick)
SSD_Update Task @10 ms
Temp_Get Task @100 ms
Button_Update Task @150 ms
Temp_Update Task @1000 ms
0
10
20
30
40
50
60
70
80
Schedulability Check

## Slide 13
Time
(200ms)
SSD_Update Task @10 ms
Temp_Get Task @100 ms
Button_Update Task @150 ms
Temp_Update Task @1000 ms
0
200
400
600
800
1000
1200
1400
1600
Schedulability Check

## Slide 14
Contacts
  Phone : 01141919874
  Email : mohameda.awwad@yahoo.com
  LinkedIn : www.linkedin.com/in/mohammed-awwad/